PANOPTICON

Technical Rider

Band Members:

Daniel Blum: Lead Vocals, Guitar

Alex Hwesta: Keyboards, Guitar, Back Vocals

Georg Wodarz: Bass, Keyboards, Back Vocals

Simos Karastefanis: Drums,Back Vocals

- Stage

Minimum size: 5 x 5 m  + PA Wings

the stage has to be solid, swingproof, be kept clear of rain or water or statically safe (500kg/m2)

- Backline

The band will provide most of the Backline themselves. In some cases, the bands will negotiate sharing the drumkit, etc.

The venue has to provide the mics that are mentioned below (see „tracks“), XLR- and instrument backup cables, DI Boxes and mic stands.

- PA

Professional PA system, well dimensioned for venue.(GRAPHIC EQ!)

The band only needs 1 console, to provide foldback monitoring.

- FOH Console:

24  (at least 16) Channels (13mono/3 Stereo); 4 band semi parametric EQ, hi-pass filters, and 4

aux sends (pre/post assignable per channel).  VCA’s and mute groups preferred but not necessary.

Monitoring: At least 4 Monitors (2 InEar/Headphones, 2 Monitor Wedges) on 2 Sends, BETTER are 4 Sends for Monitors. Lead Vox In Ear, Drummer Headphones. (GRAPHIC EQ for the Wedges > NO FEEDBACK!)

Dynamics: 3 Stereo Compressors for Bass, Base Drum, Snare, and Back Vox are preferred but not necessary.

FX:    1 Reverb, 1 Multi-FX processor (Snare, Back Vox)

The Lead Singer has his own Channelstrip + FX on Stage (can be provided pre mixed or in wet/dry 2x mono)

All our DI Signals already symmetric and need no DI Boxes except for the Lead Guitar.

Tracks:

## Channel	Source					Preferred Mic./ Output

1	Bassdrum	Audix D6 (our own)

2	Snare	Heil Sound PR22 (our own)

3	Tom 1	Audix D2 (our own)

4	Tom 2 	Audix D4 (our own)

(5	Overhead left	AKG C451 or similar) OPTIONAL

(6	Overhead right	AKG C451 or similar) 4 Small Venue

7	Bass	DI or Low Freq Mic

10	Lead Guitar 	DI from Preamp to DI BOX

(11	Lead Guitar	SM57/SM7/MD421) OPTIONAL

12	Rythm Guitar	Sennheiser SM57/e906/MD421

13	Keyboard Live	DI L

14	Keyboard Live	DI R

15	PB Keys	DI L

16	PB Keys	DI R

17	PB Percussion	DI L

18	PB Percussion	DI R

19	Lead Vocal	Beta 58 (our own)

(20)	Lead Vocals FX WET MONO DI	OPTIONAL)

21	Back Vox 1	SM58 (our own)

22	Back Vox 2	SM58 (our own)

(23	Back Vox 3	Beta 58 (our own)) OPTIONAL

Contact:

http://www.panopticon-official.com

office@panopticon-official.com

Daniel Blum: 0043 676 455 47 12

This Technical Rider is Part of the Contract!

# Text boxes

LEAD GIT

Mon 2

Mon 4

Mon 3